## Slide 1
Sound field modeling for virtual acoustics
Peter Svensson Acoustics Research Centre Department of Electronics and Telecommunications

## Slide 2: This tutorial
• Recap: the auralization block diagram Source - Impulse response - Sound rendering

## Slide 3: This tutorial
• Recap: the auralization block diagram Source - Impulse response - Sound rendering
• Computation of impulse responses for auralization
- “Exact” methods – how to use them in auralization
- Geometrical acoustics (GA) methods

## Slide 4: This tutorial
• Recap: the auralization block diagram Source - Impulse response - Sound rendering
• Computation of impulse responses for auralization
- “Exact” methods – how to use them in auralization
- Geometrical acoustics (GA) methods
• In GA: importance of specular reflections, diffuse reflections, diffraction

## Slide 5: This tutorial
• Recap: the auralization block diagram Source - Impulse response - Sound rendering
• Computation of impulse responses for auralization
- “Exact” methods – how to use them in auralization
- Geometrical acoustics (GA) methods
• In GA: importance of specular reflections, diffuse reflections, diffraction
• Demonstration of the Matlab “Edge diffraction toolbox”

## Slide 6: The auralization block diagram
/RENDERING

## Slide 7: The auralization block diagram
Footnote:
this block diagram is based on the relationship for a linear, time-invariant (LTI) system:
LTI system:
Impulse response h(t)
Transfer function H(w)
Input signal:
x(t), or X(w)
Output signal:
y(t), or Y(w)

## Slide 8: The auralization block diagram
Footnote:
this block diagram is based on the relationship for a linear, time-invariant (LTI) system:
We might want to auralize “walking around”, which means that we don’t have a “TI” system. Can usually be done by piecewise stationary models, that are interleaved. Doppler effects require some more advanced handling.
We might have a non-linear source mechanism – but the sound propagation is usually linear!

## Slide 9: The auralization block diagram
The IR can be measured or synthesized/computed.
Different formats:
Binaural (2 channels)
HOA (N channels)
Discrete directions (N channels)
Set of virtual sources
or a combination of these.
HOA = Higher-order Ambisonics = multi-channel format

## Slide 10: The auralization block diagram
The convolution can be done
- using long FIR filters (e.g. measured),
or
- with a set of individual reflections (= simple filter+delay) + simplified reverberation

## Slide 11: The auralization block diagram
The source signal can be recorded or synthesized.
Different formats:
Ref. signal + directivity data (1 channel + extra data)
HOA (N channels)
Discrete directions (N channels)

## Slide 12: The auralization block diagram
The source signal can be recorded or synthesized.
Different formats:
Ref. signal + directivity data (1 channel + extra data)
HOA (N channels)
Discrete directions (N channels)
The most common format

## Slide 13: The auralization block diagram
The source signal can be recorded or synthesized.
Different formats:
Ref. signal + directivity data (1 channel + extra data)
HOA (N channels)
Discrete directions (N channels)
The most common format
… but as argued by Otondo and Rindel, this is in principle not possible for some musical instruments.

## Slide 14: The auralization block diagram
The source signal can be recorded or synthesized.
Different formats:
Ref. signal + directivity data (1 channel + extra data)
HOA (N channels)
Discrete directions (N channels)
Otondo and Rindel suggest this format [2005].

## Slide 15: The auralization block diagram
The source signal can be recorded or synthesized.
Different formats:
Ref. signal + directivity data (1 channel + extra data)
HOA (N channels)
Discrete directions (N channels)
The so-called “O-format”, [Giron 1996], [Menzies 2002]

## Slide 16: The auralization block diagram
Different formats for the sound presentation/rendering:
Binaural, for headphones or lsp with CTC
HOA, WFS, Discrete direc-tions (VBAP), for multi lsp
CTC = Cross-talk cancellation
WFS = Wavefield synthesis
VBAP = Vector-based amplitude panning

## Slide 17: Some historical notes
Auralization system around 1980 at Chalmers (Prof. Mendel Kleiner).
Generation 1 used 50 loudspeakers: sound pres. format was “Discrete directions”. Real-time convolution by using discrete delay lines and filters for each virtual source + simplified reverberation.

## Slide 18: Some historical notes
Auralization system around 1980 at Chalmers (Prof. Mendel Kleiner).
Generation 1 used 50 loudspeakers: sound pres. format was “Discrete directions”. Real-time convolution by using discrete delay lines and filters for each virtual source + simplified reverberation.
Generation 2 used the binaural format (headphones) and long FIR-filters, but real-time convolution was not possible (then). A PDP-11 computer could convolve two channels IR of 1 s length with 10 s of anechoic music in 8 hours!

## Slide 19: Some historical notes
Auralization system around 1980 at Chalmers (Prof. Mendel Kleiner).
Generation 1 used 50 loudspeakers: sound pres. format was “Discrete directions”. Real-time convolution by using discrete delay lines and filters for each virtual source + simplified reverberation.
Generation 2 used the binaural format (headphones) and long FIR-filters, but real-time convolution was not possible (then). A PDP-11 computer could convolve two channels IR of 1 s length with 10 s of anechoic music in 8 hours!
Generation 3: In 1989, a breakthrough happened with the Austek (later Lake DSP) real-time convolver which could convolve two channels IR of 1 s length in (delayed) real-time, using FFT-based convolution.
Today real-time convolution with long FIRs and many channels is easy on a PC.

## Slide 20: Computing/synthesizing the IR using different approaches
1. Physical modeling approach – compute the sound pressure using some computer model of the physical reality. Two families of methods are used:
Wave-theoretical, “exact”, methods: FEM, BEM, FDTD etc. Well- established for computing sound fields, but still no commercial tools available for auralisation. These methods give the total sound pressure in a point, just as we would measure it.
Geometrical acoustics (GA) based: ray tracing, image source method, beam tracing, radiosity. Several commercial tools (CATT Acoustic, Odeon etc). These methods decompose the sound field into discrete components [Savioja & Svensson 2015].

## Slide 21: Computing/synthesizing the IR using different approaches
1. Physical modeling approach – compute the sound pressure using some computer model of the physical reality. Two families of methods are used:
Wave-theoretical, “exact”, methods: FEM, BEM, FDTD etc. Well- established for computing sound fields, but still no commercial tools available for auralisation. These methods give the total sound pressure in a point, just as we would measure it.
Geometrical acoustics (GA) based: ray tracing, image source method, beam tracing, radiosity. Several commercial tools (CATT Acoustic, Odeon etc). These methods decompose the sound field into discrete components [Savioja & Svensson 2015].
2. Perceptual modeling approach – generate an IR which gives a similar perceived impression as the physical reality. Can use a very simple model of reality, which is adjusted to “sound plausible”. One example: direct sound + simplified, frequency-dependent reverberation.

## Slide 22: Wave-theoretical methods, 1
Why don’t we always use these methods, if they are “exact”? They are computationally very demanding, but isn’t computation power cheap?

## Slide 23: Wave-theoretical methods, 1
Why don’t we always use these methods, if they are “exact”? They are computationally very demanding, but isn’t computation power cheap?
More demanding than we like!
Volume-element based methods:
FEM, ARD Calculation time ~ (per frequency!)
FDTD, PSTD Calculation time ~
Surface-element based methods:
BEM Calculation time ~ (per frequency!)
FMBEM Calculation time ~ (per frequency!)
Besides the high cost to reach high frequencies, we also spend most of the cost on the highest frequencies – where we don’t care so much about details!

## Slide 24: Wave-theoretical methods, 2
The quite obvious solution is to use these methods for the low-to-mid frequency range, where GA methods have problems (see later slide). [Granier et al 1996], [Kristiansen et al 2001].
A challenge is how to use the calculations for auralization.
Simplest More flexible
approach Plane Wave Decomposition
16-18 cm
Use 2 “microphones” to represent the ears

Plane wave amplitudes chosen to give the sound field in the whole domain around the head [Støfringsdal&Svensson 2006].

## Slide 25: GA-based methods, 1
The Geometrical Acoustics-based methods are dominating for auralization of indoor cases. Commercial softwares for this (CATT Acoustic, Odeon etc) have offered auralization using the binaural format since the 1990s, and later also the Higher-Order Ambisonics (HOA) format.
GA has two major limitations:
1. Finite surfaces are handled incorrectly (discontinuous wavefronts) – but for hard surfaces this can be handled by adding diffraction.
2. Impedance surfaces are handled incorrectly if they are too close to the source or receiver.
Both limitations are most important at low frequencies. Limitation 1 also for higher frequencies, for some geometries (e.g. behind a screen).

## Slide 26: GA-based methods, 2
The GA-based methods also have very clear advantages:
• Commercially available software, with (almost) all auralization tools needed.
• Simplified calculations possible (few rays in ray tracing), to get a rough idea of how a room will sound.
• Ray tracing can handle the important diffuse reflections/scattering and late reverberation.
• Some source directivity data is easily available.
• Quite much absorption data is easily available. But! Only absorption coefficients from 125 Hz to 4 kHz! Scattering coefficients more difficult to find.
• Market open for the development of open-source tools!

## Slide 27: GA-based methods, 3a
The diffraction phenomenon is illustrated by these two animations (made with the Edge diffraction toolbox by the author):
Shoebox room with two ceiling reflectors.
Specular reflections only (<=order 6): Specular reflections and diffraction (order 1):

## Slide 28: GA-based methods, 3a
Specular reflections imply truncated wavefronts, which are clearly unphysical, and this error might be important or less important. Examples on next slide.
The diffraction phenomenon is illustrated by these two animations (made with the Edge diffraction toolbox by the author):
Shoebox room with two ceiling reflectors.
Specular reflections only (<=order 6): Specular reflections and diffraction (order 1):

## Slide 29: GA-based methods, 3a
We can inspect the response (IR and TF) in two different receiver positions.
The diffraction phenomenon is illustrated by these two animations (made with the Edge diffraction toolbox by the author):
Shoebox room with two ceiling reflectors.
Specular reflections only (<=order 6): Specular reflections and diffraction (order 1):

## Slide 30: GA-based methods, 3a
We inspect the responses in two different points.

## Slide 31: GA-based methods, 3a
We listen to the “pinkified” impulse responses in two different points.

## Slide 32: GA-based methods, 3a
Conclusions/insights:
• GA solutions can look suspicious (truncated wavefronts), but as long as there are quite many reflections that hit a receiver, diffraction might change the perceived sound quite little.
• In receiver positions that are hidden behind objects, GA solutions might give substantial errors.
• Listening examples show that reverberation (higher-order reflections) is usually necessary for a chance of natural sound!

## Slide 33: GA-based methods, 3a
If surfaces are rough instead of plane, then reflections get diffuse, which means sound spreads in all frontal directions, but not around corners!.
The diffraction phenomenon is illustrated by these two animations (made with the Edge diffraction toolbox by the author):
Shoebox room with two ceiling reflectors.
Specular reflections only (<=order 6): Specular reflections and diffraction (order 1):

## Slide 34: GA-based methods, 3b
Another example made with the Edge diffraction toolbox: a cylinder
The finer geometrical models we make, the higher order diffraction we need!
GA only Incl. D1 Incl. D2 Incl. D3

## Slide 35: GA-based methods, 3b
Another example made with the Edge diffraction toolbox: a cylinder
The finer geometrical models we make, the higher order diffraction we need!
We can study the sound field along a line behind the cylinder.
GA only Incl. D1 Incl. D2 Incl. D3

## Slide 36: GA-based methods, 3b
We can observe large differences between D2 and D3 at 252 Hz, but much less at 1998 Hz. So, higher-order diffraction is most important at low frequencies!
Again: the smaller the details we include in a model, the higher the order of diffraction we might need.

## Slide 37: GA-based methods, 4
Some examples from presentations by others. These are all examples showing interactive applications.
Interactive simulation of large-scale acoustic environment with a moveable receiver, with only specular reflections [Funkhouser et al 1999]. See http://www.cs.princeton.edu/~funk/acoustics.html SPECULAR ONLY
2008 Simulation of interaction (moveable receiver and source) of very complex geometries with specular reflections and low-order diffraction [Chandak et al 2008]. See https://www.youtube.com/watch?v=3aqSB-Ocr04. SPECULAR + LOW-ORDER DIFFRACTION
2014 Simulation of interaction of very complex geometries with specular reflections, diffuse reflections, and medium-order diffraction [Schissler et al 2014]. See https://www.youtube.com/watch?v=XJemYHeeZpc SPECULAR+DIFFUSE+HIGH-ORDER DIFFRACTION

## Slide 38: The Edge Diffraction Toolbox
Implemented in Matlab since late 1990s; freely available. Primitive GUI: script-file input for setting parameters etc. Uses CAD-file format defined by CATT Acoustics (“Corners” and “Planes”).
Two distinct versions:
• “EDBtoolbox” for time- and frequency-domain calculations. Image source method + diffraction. Calc. time increases exponentially with reflection/diffraction order. Based on publications from 1999,2002,2006.
Can handle low reflection orders for large models, or quite high reflection orders for small models.
• “ESIEtoolbox” for frequency-domain calculations, for convex scatterers. Calc time increases linearly with diffraction order. Based on an integral equation formulation published in 2013. Time-domain formulation published in 2014 but not implemented in the toolbox yet.
The EDBtoolbox was used for the animations: one IR calculated for each of ≈ 10000 receiver positions.
URL: http://www.iet.ntnu.no/~svensson/software/index.html#EDGE

## Slide 39
Example with the ESIE toolbox - Sphere

## Slide 40: Numerical example 2 – six-sided disc
Receiver on the disc. Source 10 radii away.
We compare the accuracy of the FD and the TD formulation (by taking an FFT of the TD results). [Svensson & Asheim 2013]
Reference solution 32 Gauss-Legendre discretization points per edge.
Two errors expected for the TD version
Spatial discretization: ≈ constant up to a certain frequency with N elements per wavelength, and then rapidly increasing error.
Time discretization: with a first-order TD discretization, we expect a +6 dB per octave error.

## Slide 41: Numerical example 2 – six-sided disc
Similar error for the TD and the FD solutions at LF – but, error increases for higher frequencies with the TD solution.

## Slide 42: Numerical example 2 – six-sided disc
Similar error for the TD and the FD solutions at LF – but, error increases for higher frequencies with the TD solution.
If the sampling frequency is increased 4x, then the TD error reaches the FD error.
But…… a higher sampling frequency is costly.

## Slide 43: So, how should we auralize indoors cases?
Depends on accuracy requirements (and available computation time)!
• Level 1 – Use direct sound + simplified reverberation with the right T60, and frequency-dependence.
• Level 1.5 – Use direct sound + very few, very early reflection/diffraction effects + simplified reverberation.
• Level 2 – Use detailed geometrical acoustics model, and diffuse+specular reflections (important to do both). Commercial tools available.
• Level 3 – Augment the GA (from level 2) with diffraction in challenging cases. Commercial tools available.
• Level 4 – Augment the GA + diffraction with Wave-theoretical calculations at low frequencies. You will need to do some programming!

## Slide 44: References
A. Chandak, C. Lauterbach, M. Taylor, Z. M. Ren, and D. Manocha: "AD-Frustum: Adaptive Frustum Tracing for Interactive Sound Propagation," IEEE Trans Vis Comp Graph 14, pp. 1707-1714, 2008.
T. Funkhouser, P. Min, and I. Carlbom: "Real-time acoustic modeling for distributed virtual environments," Proc. of ACM Computer Graphics, Siggraph 99, pp. 365-374, 1999.
F. Giron: "Investigations about the directivity of sound sources," PhD thesis, Ruhr University, Bochum, 1996.
E. Granier, M. Kleiner, B.-I. Dalenbäck, and P. Svensson: "Experimental auralization of car audio installations," J. Audio Eng. Soc. 44, pp. 835-849, 1996.
U. Kristiansen, H. Dong, U. P. Svensson, E. Vernet, and J.-N. Liabeuf: "Calculating sound impulse responses in city streets," in Proc. of the 17th Intern. Congress on Acoust., Rome, 2001.
D. Menzies: "W-panning and o-format, tools for object spatialization," in Proc. of 22nd AES Int. Conf., Helsinki, 2002.
F. Otondo, J. H. Rindel: "A new method for the radiation representation of musical instruments in auralizations," Acta Acustica/Acustica 91, pp. 902-906, 2005.
L. Savioja, U. P. Svensson: “Overview of geometrical room acoustic modeling techniques,” J. Acoust. Soc. Am. 138, pp. 708-730, 2015.
C. Schissler, R. Mehra, and D. Manocha: "High-order diffraction and diffuse reflections for interactive sound propagation in large environments," ACM Transactions on Graphics (TOG) - Proceedings of ACM SIGGRAPH 2014 33, Article 39, 2014.
B. Støfringsdal, U. P. Svensson: "Conversion of discretely sampled sound field data to auralization formats," J. Audio Eng. Soc. 54, pp. 380-400, 2006.
U. P. Svensson, A. Asheim: "Time-domain formulation of an edge source integral equation," in Proc. of ICA2013, Montreal, 2013.