## Slide 1: Green competitiveness in the silicon industry?
Climate change has gone from If to When to Now (World Bank)
Everyone is entitled to his/her own opinion, but not his/her own facts.
Professor Leiv Kolbeinsen, Dep. Mat. Sci. & Eng., NTNU

## Slide 2: Content of this presentation
Metal production: Reductants/Energy sources
The system Earth is not closed with respect to energy
The Renewable energy leader globally
Silicon Use and Production
Silicon production, Si production and CO2 emissions, “Triple bypass”, The Solsilc process and The Elkem Solar Route
GasFerroSil
Green (Si-production) economy examples:
Elkem: Carbon Neutral Metal Production (CNMP)/Finnfjord
Sustainable Business Models – Industrial Symbiosis (Clusters)
Summing up

## Slide 3: Metal production: Reductants/Energy sources
Stolen from Jean-Pierre Birat (and adapted by me)
Carbon
Hydrogen
Electrones
Coke
Coal
Natural Gas
SynGas
H2
H2 from water electrolysis
Electricity
Blast furnace + plasma
Ferro-alloys/silicon & Aluminium
Electro steel (EAF)
NG reduction
BlastFurnace (BF)
H2 reduction
Electrolysis
Decarburization

## Slide 4: The system Earth is not closed with respect to energy
The annual global energy consumption, for 2009, was estimated at 16 TW-yrs (or 140,160,000,000 KW-hrs) illustrated by the orange sphere on the left-most side

## Slide 5: The Renewable energy leader globally ICRIER Working Paper 329 Ashok Gulati, Stuti Manchanda, Rakesh Kacker: Harvesting Solar Power in India! Aug 2016
Germany – The Renewable energy leader in total cumulative installations globally and leads by a successful model. In 2014:
Germany’s 38 GW accounts for nearly 21percent of total solar installed capacity in the world (2014). All this makes Germany a key leader in solar power.
There are 2 key elements in Germany’s solar power success that have contributed to substantial rooftop installations:
guaranteed grid connection to renewable energy producers and
Feed-in-Tariffs (FITs)
By 2013,
23 percent of global residential solar rooftops and
37 percent of global commercial solar rooftop
installations took place in Germany*. Governed by the Renewable Energy Sources Act 2000 (Erneuerbare-Energien-Gesetz EEG), renewables including solar enjoy priority grid connection and are supported through Feed-in-Tariffs (FITs) in Germany. This has enabled even the small producers and farmers to connect to the grid and earn revenue by selling solar power.
* http://marketrealist.com/2015/02/german-rooftops-domniate-global-photovoltaic-capacity/ (Accessed: 6th June 2016)
Country | Cumulative installed solar capacity [GW] | MW/million people
Germany | 38 | 469
China | 28 | 20
Japan | 23 | 181
India | 3 | 2.3

## Slide 6: Silicon is used in a number of processes/applications
• Ferrosilicon is used both for removing oxygen from liquid steel and cast iron (de-oxidation), as well as being an alloying element. The end-users are the automotive and construction companies.
• Silicon is mainly used for alloying other metals, especially aluminium (about 45 % of global silicon production is for alloying purposes). As for ferrosilicon, the end-users are automotive and construction companies.
• Silicon is also used as feedstock for the silicone industry (about 40 %). The end products are typically cosmetics, construction, anti-foam, medical equipment, automotive parts, etc.
• Silicon is an essential ingredient in semiconductors and in the solar industry (about 10-15 % and growing). In electronic equipment, the amount of pollution elements must be as low as in the ppb (parts per billion) range. More than 90 % of all electronic components are based on silicon. Another important market for the industry is silicon used in solar cells. Here the pollution level is in the ppm (parts per million) range.

## Slide 8: Si production and CO2 emissions
Electricity source | Total spec. CO2 (kg CO2/kg Si)
Theoretical C - free | [1.6 (1CO2/Si)] – 3.2 (2 CO => 2CO2/Si)
Hydro/Nuclear | 4.3
Gas Power | 10.6
Coal power | 17.7
SiO2(s)+(1+x)C(s) = xSi+(1-x)SiO(g)+(1+x)CO(g)

## Slide 9
Elkem sustainability report 2014
Main steps in the Si-process (Elkem)

## Slide 10: The Solsilc process

## Slide 11: The Elkem Solar Route

## Slide 12: What happens when cold CH4 (g) meets hot SiO (g)?
Based on a paper by B. Monsen, L. Kolbeinsen, S. Prytz, V. Myrvågnes, and K. Tang at the INFACON conference in Kazakhstan June 2013

## Slide 13: Theory
Practice
Based on a paper by B. Monsen, L. Kolbeinsen, S. Prytz, V. Myrvågnes, and K. Tang at the INFACON conference in Kazakhstan June 2013

## Slide 14: GasFerroSil project
Oxygen in Silica is used to convert CH4 to “Syn Gas” (H2 + CO) with Si as bi-product

## Slide 15: Green = Circular?

## Slide 16: Elkem: Carbon Neutral Metal Production (CNMP)
Elkem sustainability report 2015

## Slide 17: Elkem: Carbon Neutral Metal Production (CNMP)

## Slide 19: Finnfjord Vision
World’s largest ferrosilicon producer without CO2 emissions

## Slide 20: Ambitious
Remote

## Slide 21: Sustainable business models

## Slide 22: Green Clusters – Industry Symbiosis
Corporation C
Corporation A
Corporation B

## Slide 23: Industrial Cluster or Symbiosis – links
Raw 2
Raw 1
Corporation C
Corporation A
Corporation B
Main prod.
Waste
Bi-prod.
Bi-prod.
Bi-prod.
Prod.
Prod.
Waste
Waste

## Slide 24: The corporations are made of Processes
Process A2
Process A3
Process A4
Process A1
Process A5
Process B5
Process B4
Process B3
Process B2
Process B1
Process C1
Process C2
Process C4
Process C3
Corporation C
Corporation A
Corporation B

## Slide 25: “New” corporations by rearranging “old” processes
Process A3
Process A4
Process A5
Process B5
Process B4
Process B3
Process B2
Process B1
Process A2
Process A1
Process C1
Process C2
Process C4
Process C3

## Slide 26: The 2052 Forecast: What will happen? How can metal production contribute?
Make sure production does not include any fossil inputs
Make sure process is suited for solar power – i.e. direct current and intermittent power
Make sure there exist technologies (like CCS) to neutralize greenhouse gas emissions (e.g. CO2 and CH4)
Work for a global ban on metals made from fossil fuels – or at least labelling of climate friendly metals
Jorgen Randers Professor Emeritus Climate Strategy BI Norwegian Business School

## Slide 27: Metal production: Reductants/Energy sources
Stolen from Jean-Pierre Birat (and adapted by me)
Carbon
Hydrogen
Electrones
Coke
Coal
Natural Gas
SynGas
H2
H2 from water electrolysis
Electricity
Blast furnace + plasma
Ferro-alloys/silicon & Aluminium
Electro steel (EAF)
NG reduction
BlastFurnace (BF)
H2 reduction
Electrolysis
Decarburization
Possible development?

## Slide 28
Hi, name is Mingus,
Thank you for listening to my «daddy»!